## Slide 1
Kevin Grant
NEFI – GHG emissions goals
November 5, 2019

## Slide 2: Discussion points
Historical Greenhouse Gas Emissions
Estimated GHG targets vs. NEFI goals
Renewable heating oil blend scenarios
Path to achieving goals and potential obstacles
Framing the debate on liquid heating fuels

## Slide 3: Greenhouse Gas Emissions
https://www.epa.gov/sites/production/files/2019-04/documents/us-ghg-inventory-2019-main-text.pdf

## Slide 4: EPA GHG figures for 1990 and 2017
GHG Emissions by sector

## Slide 5: EPA GHG figures for 1990 and 2017
Comparison of total GHG for all sectors vs. residential only

## Slide 6: GHG gas reductions by product
Lifecycle Analysis Greenhouse Gas Results for Select Pathways (kg CO2e per mmBtu) |  |  | 
Feedstock | Fuel | Production Process | Percent Reduction
Algal oil | Biodiesel | Transesterification (Open Pond, Mid) | 66%
Algal oil | Biodiesel | Transesterification (PBR, Mid) | 71%
Barley | Ethanol | Dry Mill (<36,800 Btu/gal NG, <0.19 kWh/gal Elec.) | 51%
Barley | Ethanol | Dry Mill NG | 47%
Biogas from landfills | Renewable electricity | Any | 87%
Canola oil | Biodiesel | Transesterification | 50%
Cellulose from corn stover | Cellulosic diesel | Fischer-Tropsch process | 91%
Cellulose from corn stover | Ethanol | Biochemical enzymatic process | 129%
Corn starch | Butanol | Dry Mill Biomass (dry DDGS) | 50%
Corn starch | Butanol | Dry Mill NG Base Plant (dry DDGS) | 27%
Corn starch | Butanol | Wet Mill Coal | 8%
Corn starch | Ethanol | Dry Mill Biomass (2022 Average) | 38%
Corn starch | Ethanol | Dry Mill NG (2022 Average) | 21%
Corn starch | Ethanol | Wet Mill Coal | -19%
Grain sorghum | Ethanol | Dry Mill, 92% Wet DGS, Biogas, CHP | 53%
Grain sorghum | Ethanol | Dry Mill, Dry DGS, NG | 22%
Palm oil | Biodiesel | Transesterification | 17%
Palm oil | Renewable diesel | Hydrotreating | 11%
Soybean oil | Biodiesel | Transesterification | 57%
Sugarcane | Ethanol | Fermentation (Trash, No CBI, Marg. Elec.) | 91%
Sugarcane | Ethanol | Fermentation (No Trash, No CBI, Marg. Elec.) | 61%
Switchgrass | Cellulosic diesel | Fischer-Tropsch process | 71%
Switchgrass | Ethanol | Biochemical enzymatic process | 110%
Switchgrass | Ethanol | Thermochemical gasification process | 72%
Yellow grease | Biodiesel | Transesterification | 86%
Petroleum | Baseline Gasoline | Refining | 0%
Petroleum | Baseline Diesel | Refining | 0%
https://www.epa.gov/fuels-registration-reporting-and-compliance-help/lifecycle-greenhouse-gas-results

## Slide 7: Bio blends required to hit targets
15% GHG reductions from 1990 levels
15% GHG reductions from 1990 residential levels

## Slide 8: Bio blends required to hit targets
40% GHG reductions from 1990 residential levels

## Slide 9: Northeast biodiesel volume requirements to meet GHG reduction goals

## Slide 10: Necessary steps to achieve goals
1) Capital Investment
  Expansion of production / transport / storage assets
  Third party blending facilities in major ports
  Shipping companies addition of bio barges
  Increase in rail infrastructure and trucking capacity
2) Access to waterborne
  Availability of domestic and European material
  “We are going to need a bigger boat...”
  Access to Argentina biodiesel
3) Increased regional production
  Local production currently has limited elasticity
  2020 - 2021 start dates necessary to meet goals
4) Combined efforts to meet targets
  Reseller and wholesaler blending
  Lobbying coordination on bio tax credit

## Slide 11: Additional issues
Pipelines
  Jet line / Colonial
  Stranded terminals
Petroleum supply from non RFS locations
  Canadian vessels and rail (VT)
  Heating oil imports during peak periods
  Common sense rules
Managing the increase in cost
  Storage costs – heating / segregation
  Possible decrease in loading locations
  Bio premiums in short market
New Products
  Blend stocks with lower GHG profile likely to be required
Adjusting to change in traditional heating oil supply chain

## Slide 12: GHG emissions by sector in U.S.

## Slide 13: Massachusetts emissions by sector
Massachusetts Household Heating |  | 
Fuel Type | # of Households | Percentage
utility gas | 1,321,175 | 50.6%
bottled, tank, LP | 83,401 | 3.2%
electricity | 395,373 | 15.3%
fuel oil, kerosene | 707,835 | 27.4%
coal or coke | 2,851 | 0.1%
wood | 40,176 | 1.6%
solar | 1,984 | 0.08%
other fuel | 20,025 | 0.8%
no fuel | 12,895 | 0.5%
total | 2,585,715 | 
http://www.mass.gov/eea/docs/dep/air/climate/1990-2020-final.pdf

## Slide 14: New York State GHG Emissions
NYSERDA - New York State Greenhouse Gas Inventory: 1990–2016 Final Report | July 2019